## Slide 1: Number Representation in Digital Systems 05/03/2013
INTRODUCTION TO DIGITAL SYSTEMS

## Slide 2: OUTLINE
1. Number systems
  Decimal Number
  Binary Number
  Hexadecimal Number
  Octal Number
2. Number systems conversion
3. Binary Operations
4. Signed numbers Representation
5. Other representations
  Floating Point Number
  BCD
  ASCII

## Slide 3: 1. Number systems
Decimal Number
Binary Number
Hexadecimal Number
Octal Number

## Slide 4
Number systems | Radix or base | Digits
Decimal | 10 | 0, 1, 2, 3, 4, 5, 6, 7, 8, 9
Binary | 2 | 0, 1
Octal | 8 | 0, 1, 2, 3, 4, 5, 6, 7
Hexa-decimal | 16 | 0, 1, 2, 3, 4, 5, 6, 7, 8, 9 A, B, C, D, E, F
Number systems

## Slide 5: Decimal
weight
weight
weight
weight
weight
Decimal point

## Slide 6: Decimal
Ex: analyze decimal number 2745.21410
2745.21410 =
2 * 103 + 7 * 102 + 4 * 101 + 5 * 100 +
2 * 10-1 + 1 * 10-2 + 4 * 10-3
Decimal point

## Slide 7: Binary
weight
weight
weight
weight
weight
Binary point

## Slide 8: Binary
Ex: Analyze binary number 1011.1012
1011.1012 =
1 * 23 + 0 * 22 + 1 * 21 + 1 * 20 +
1 * 2-1 + 0 * 2-2 + 1 * 2-3 = 11.62510
Binary point

## Slide 9: Octal
Ex: Analyze octal number 3728
3728 =
3 * 82 + 7 * 81 + 2 * 80 = 25010

## Slide 10: Hexadecimal
Ex: Analyze hex number 3BA16
3BA16 =
3 * 162 + 11 * 161 + 10 * 160 = 95410

## Slide 11: Example
Một người chạy bộ chạy quanh hồ con rùa muốn sử dụng 10 ngón tay của mình để đếm số vòng chạy được. Người này có thể đếm bao nhiêu vòng một cách thuận tiện? Giải thích ngắn gọn câu trả lời của bạn.

## Slide 12: Number system conversion

## Slide 13: Convert to decimal
Multiply each digit with its weight

## Slide 14: Example
Express 37028 in decimal
  37028 = 2 * 80 + 0 * 81 + 7 * 82 + 3 * 83 = 198610
Express 1A2F16 in decimal
  1A2F16 = 15 * 160 + 2 * 161 + 10 * 162 + 1*163 =670310

## Slide 15: Decimal => Binary
Divide by 2 and write down the remainder
  Until a quotient of 0 is obtained
First remainder as LSB (Least significant bit)
Last remainder as MSB (Most significant bit)
Decimal
Binary

## Slide 16: Example: 2510 => binary

## Slide 17: Decimal => Hexadecimal
Decimal
Hexadecimal
Divide by 16 and write down the remainder
  Until a quotient of 0 is obtained
First remainder as LSD (Least significant digit)
Last remainder as MSB (Most significant digit)

## Slide 18: Example: 42310 => hexadecimal

## Slide 19: Decimal => Octal
Decimal
Octal
Divide by 8 and write down the remainder
  Until a quotient of 0 is obtained
First remainder as LSD (Least significant digit)
Last remainder as MSB (Most significant digit)

## Slide 20: Octal => Binary
Individually convert each digit to its 3 bit binary
Ex:
Binary
Octal
Octal | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Binary | 000 | 001 | 010 | 011 | 100 | 101 | 110 | 111

## Slide 21: Hexadecimal => Binary
Individually convert each digit to its 4 bit binary
Ex:
Binary
Hexadecimal
Hex | Bin
0 1 2 3 4 5 6 7 8 9 A B C D E F | 0000 0001 0010 0011 0100 0101 0110 0111 1000 1001 1010 1011 1100 1101 1110 1111

## Slide 22: Binary => Octal
Group 3 bits starting at LSB
Convert each group to 1 octal digit
Ex: 10110101112 => octal
Binary
Octal

## Slide 23: Binary => Hexadecimal
Group 4 bits starting at LSB
Convert each group to 1 hexadecimal digit
Ex: 101011010101110011010102 => hexa
Binary
Hexadecimal

## Slide 24: Octal <=> Hexadecimal
Hexadecimal
Octal
Binary
Convert via binary

## Slide 25: Example: 1F0C16 => octal

## Slide 26: Example: 10768 => hexa

## Slide 27: Example
Number system conversion practice
Decimal | Binary | Octal | Hexadecimal
35 |  |  | 
 | 1101101 |  | 
 |  | 712 | 
 |  |  | 1AF

## Slide 28: Fraction
Decimal => Binary

## Slide 29: Example: 189.02310 => binary

## Slide 30: Example
Another number system conversion practice
Decimal | Binary | Octal | Hexadecimal
29.8 |  |  | 
 | 110.1101 |  | 
 |  | 3.07 | 
 |  |  | C.82

## Slide 31: Binary Operations
Addition
Multiplication
Subtraction

## Slide 32: Binary Addition
2 1-bit binary numbers addition
A | B | A + B
0 0 1 1 | 0 1 0 1 | 0 1 1 10

## Slide 33: Binary Addition
2 unsigned binary numbers addition

## Slide 34: Binary multiplication
2 1-bit binary numbers multiplication
A | B | A * B
0 0 1 1 | 0 1 0 1 | 0 0 0 1

## Slide 35: Binary multiplication
2 unsigned binary numbers multiplication

## Slide 36: Binary Subtraction
The rules for binary subtraction are
0 - 0 = 0
1 - 1 = 0
1 - 0 = 1
10 - 1 = 1 with a borrow of 1
Ex: Subtract the binary number 00111 from 10101
00111 7
10101 21
0
1
1
1
0
14
=

## Slide 37: Signed number representation
Signed Number Representation
1’s complement form
2’s complement form
2’s complement to binary
Operations in the 2’s complement system
Overflow

## Slide 38: Signed Number Representation
Signed numbers are positive (+) or negative (-)
Some means to represent the sign
Use 1 additional bit to represent the sign (sign bit)
  0: positive
  1: negative
Sign bit is often the leftmost bit

## Slide 39: Signed Number Representation
Example: a 6 bit signed number

## Slide 40: 2’s complement
2’s complement is the most commonly way used to represent signed numbers
Binary
1’s complement
2’s complement
Ex:
0 1 0 0 1 0 0 1 0 0 (29210)
Negate each bit
1 0 1 1 0 1 1 0 1 1 (-29210)
Add 1
1 0 1 1 0 1 1 1 0 0 (-29210)
+1

## Slide 41: Representing signed numbers using 2’s complement

## Slide 42: Example
Representing signed numbers using 2’s complement
  +13
  -9
  -2
  -8

## Slide 43: Converting 2’s complement to binary
Binary
2’s complement
Binary
Ví dụ:
1 0 1 1 0
0 1 0 1 0
Negate each bit
Add 1
1 0 1 1 0
Negate each bit
Add 1

## Slide 44: Addition in the 2’s complement system
Just like binary addition
  Sign bit is operated on in the same manner as the magnitude bits
  If a carry is generated in the last position, this carry is always disregarded
  If the final result is negative, it is in 2’s complement form

## Slide 45: Example

## Slide 46: Example
+9 and -9 addition?

## Slide 47: Subtraction in the 2’s complement system
In an example 4 + (–9), addition in the 2’s complement system is actually subtraction
Subtraction in the 2’s complement system
  Take the 2’s complement of the subtrahend (including sign bit)
  It is added to the minuend
  The result of this addition represents the required difference

## Slide 48: Example
9 – 4 =
Take the 2’s complement
9 + (– 4)
  Add it to the minuend

## Slide 49: Arithmetic Overflow
Overflow occurs when the number of bits required for the answer is exceeded
  n bit represents a number from -2n-1 to +2n-1-1
  Overflow always produces an incorrect result
=> A special circuit is used to detect any overflow condition

## Slide 50: Overflow examples
4 bit numbers, 3 magnitude bit and 1 sign bit
Overflow never occurs if numbers have different signs
O
O

## Slide 51: Other Codes
BCD
Floating point number
ASCII

## Slide 52: BCD (Binary coded decimal)
Each digit of a decimal number is represented by its binary equivalent
Ex:
84710 => BCD
1010 => BCD
0001
0000
1
0

## Slide 53: BCD vs. Binary
BCD uses more bit, yet the conversion is simpler
13710 = 100010012 (Binary)
Decimal: 1 * 27 + 1 * 23 + 1 * 20
13710 = 0001 0011 0111 (BCD)
Decimal: 1 3 7

## Slide 54: BCD
A lab experiment in which BCD is converted to decimal is shown.

## Slide 55: Floating Point Number
Floating point notation is capable of representing very large or small numbers by using a form of scientific notation.
A 32-bit single precision number is illustrated.
S E (8 bits) F (23 bits)
Sign bit
Magnitude with MSB dropped
Biased exponent (+127)

## Slide 56: Floating Point Number
Express the speed of light, c, in single precision floating point notation. (c = 0.2998 x 109)
In scientific notation,
c = 1.001 1101 1110 1001 0101 1100 0000 x 228.
0 10011011 001 1101 1110 1001 0101 1100
In binary, c = 0001 0001 1101 1110 1001 0101 1100 00002.
S = 0 because the number is positive.
E = 28 + 127 = 15510 = 1001 10112.
F is the next 23 bits after the first 1 is dropped.
In floating point notation, c =

## Slide 57: ASCII

## Slide 58: Digital Key Terms
Byte
Floating-point number
Hexadecimal
Octal
BCD
A group of eight bits
A number representation based on scientific notation in which the number consists of an exponent and a mantissa.
A number system with a base of 16.
A number system with a base of 8.
Binary coded decimal; a digital code in which each of the decimal digits, 0 through 9, is represented by a group of four bits.
Alphanumeric
ASCII
Consisting of numerals, letters, and other characters
American Standard Code for Information Interchange; the most widely used alphanumeric code.