## Slide 1: Combinational Circuits II
01/2013
Phan Quoc Huy

## Slide 2: Content
5.5 Decoder/Encoder
5.6 Multiplexer/ Demultiplexer
5.7 Parity Generator/ Checker
5.8 Comparator

## Slide 3: Reading Assignments
5.5 Chapter 5 (section 5.4, 5.5)
5.6 Chapter 5 (section 5.7)
5.7 Chapter 5 (section 5.8)
5.8 Chapter 5 (section 5.9)

## Slide 4: 5.5 Decoder/ Encoder

## Slide 5: Decoder
Multiple-input/multiple-output device
Inputs (n) are less than outputs (m)
Converts input code words into output code words
One-to-One mapping:
  Each input code produces only one output code
Input codes:
  Binary Code
  Your Code!
Output Codes
  1-out-of-m code
  Gray Code
  BCD Code
enable inputs

## Slide 6: Display Decoders
Seven segment display for decimal digits
Design the decoder:
  Input: BCD
  Output: Seven segment display
How many inputs?
SOP?

## Slide 7: Binary Decoders
n-to- 2n decoder: n inputs and 2n outputs
  Input code: n bit Binary Code
  Output code: 1-out-of- 2n , One output is asserted for each input code
Example: n=2, 2-to-4 decoder
Note “x” (don’t care input notation)

## Slide 8: Binary 2-to-4 decoder

## Slide 9: MSI Binary 2-to-4 decoder: 74x139
Input buffering (less load)
NAND gates (faster)

## Slide 10: 74x139 : Logic Symbol -Truth Table
Active Low Enable, Active Low outputs
G
Y0
Y1
Y2
Y3
A
B
Truth Table Logic Symbol Inputs Outputs G_L B A Y3-L Y2-L Y1-L Y0_L 1 X X 1 1 1 1 0 0 0 1 1 1 0 0 0 1 1 1 0 1 0 1 0 1 0 1 1 0 1 1 0 1 1 1
G_L
A
B
Y0_L
Y1_L
Y2_L
Y3_L
1/2 74x139

## Slide 11: Complete 74x139 Decoder

## Slide 12: 74x138: 3-to-8 Binary decoder

## Slide 13: 74x138: Logic Symbol

## Slide 14: 74x138: Truth Table

## Slide 15: Decoders as logic function generators
Advantages:
  Flexibility
  Multiple-output Logic functions
Disadvantages:
  Complexity: for large number of inputs
    (5-variable Function with 3 minterms! F= AB’CD’E + A’BC’DE+A’BCDE’)

## Slide 16: Implementing the Canonical Sum
The binary decoder generates all minterms of n-variable logic function
The canonical sum (sum of minterms) of a logic functions is obtained by adding all minterms of that function:
  Match the order of input bits
  Activate Enable inputs
Example :
G2A
Y0
Y1
Y2
Y3
A
B
Z
Y
74x138
Y4
Y5
Y6
Y7
C
X
G2B
G1
F
+5V

## Slide 17: Decoder cascading
4-to-16 decoder

## Slide 18: Decoder applications
Microprocessor memory systems
  selecting different banks of memory
Microprocessor input/output systems
  selecting different devices
Microprocessor instruction decoding
  enabling different functional units
Memory chips
  enabling different rows of memory depending on address
Lots of other applications

## Slide 19: Encoders
Multiple-input/multiple-output device
Performs the inverse function of a Decoder
Outputs ( m ) are less than inputs ( n )
Converts input code words into output code words
input code
output code
ENCODER

## Slide 20: Encoders vs. Decoders
Decoder
Encoder
2^n-to-n encoder
Input code: 1-out-of-2^n
Output code: Binary Code
n-to-2^n
Input code : Binary Code
Output code :1-out-of-2^n
Binary decoders/encoders

## Slide 21: Binary Encoder
2^n-to-n encoder : 2^n inputs and n outputs
  Input code: 1-out-of-2^n
  Output code: Binary Code
Example: n=3, 8-to-3 encoder
Inputs Outputs
I0 I1 I2 I3 I4 I5 I6 I7 Y2 Y1 Y0 1 0 0 0 0 0 0 0 0 0 0 0 1 0 0 0 0 0 0 0 0 1 0 0 1 0 0 0 0 0 0 1 0 0 0 0 1 0 0 0 0 0 1 1 0 0 0 0 1 0 0 0 1 0 0 0 0 0 0 0 1 0 0 1 0 1 0 0 0 0 0 0 1 0 1 1 0 0 0 0 0 0 0 0 1 1 1 1
I1
I2
I3
Y1
Y2
I4
I5
I6
I0
Y0
I7
Binary encoder

## Slide 22: 8-to-3 encoder Implementation
Simplified implementation: Y0 = I1 + I3 + I5 + I7 Y1 = I2 + I3 + I6 + I7 Y2 = I4 + I5 + I6 + I7
Limitations:
  I0 has no effect on the output
  Only one input can be activated
Application:
  Handling multiple devices requests. But, no simultaneous requests
  Establishing priorities to solve the problem of multiple requests
I1
I2
I3
I4
I5
I6
I0
I7
Y1
Y0
Y2

## Slide 23: Need priority in most applications

## Slide 24: Priority Encoder
Assign priorities to the inputs
When more than one input are asserted, the output generates the code of the input with the highest priority
Priority Encoder: H7=I7 (Highest Priority) H6=I6.I7’ H5=I5.I6’.I7’ H4=I4.I5’.I6’.I7’ H3=I3.I4’.I5’.I6’.I7’ H2=I2.I3’.I4’.I5’.I6’.I7’ H1=I1. I2’.I3’.I4’.I5’.I6’.I7’ H0=I0.I1’. I2’.I3’.I4’.I5’.I6’.I7’ IDLE= I0’.I1’. I2’.I3’.I4’.I5’.I6’.I7’
Encoder A0=Y0 = H1 + H3 + H5 + H7 A1=Y1 = H2 + H3 + H6 + H7 A2=Y2 = H4 + H5 + H6 + H7
I6
I5
I4
Y1
Y0
I3
I2
I1
I7
Y2
I0
Binary encoder
I6
I5
I4
I3
I2
I1
I7
I0
Priority Circuit
H6
H5
H4
H3
H2
H1
H7
H0
IDLE
I6
I5
I4
I3
I2
I1
I7
I0
A1
A0
A2
IDLE
Priority encoder

## Slide 25: 8-input priority encoder
I7 has the highest priority, I0 least
A2-A0 contain the number of the highest-priority asserted input if any
IDLE is asserted if no inputs are asserted

## Slide 26: 74x148 8-input priority encoder

## Slide 27: 74x148 8-input priority encoder
  Active-low I/O
  Enable Input
  “Got Something": Group Select
  Enable Output

## Slide 28: 74x148 Truth Table

## Slide 29: 74x148 circuit

## Slide 30: Cascading priority encoders
32-input priority encoder

## Slide 31: 5.6 Multiplexer/ Demultiplexer

## Slide 32: Multiplexers (Mux)
Select one of n sources of data to transmit on a bus
E.g. Put between Processor’s registers and ALU
A 16-bit processor where 3-bit field specifies one of 8 registers
The 3-bit field is connected to the select inputs of an 8-input, 16-bit Mux

## Slide 33: MSI: 74x151 8-input 1-bit multiplexer

## Slide 34: 74x151 truth table

## Slide 35: Other multiplexer varieties
2-input, 4-bit-wide
  74x157
4-input, 2-bit-wide
  74x153

## Slide 36: Demultiplexers same as decoders
A Mux is used to select one of n sources of data to transmit on a bus
A demultiplexer can be used to route the bus data to one of m destinations. Just the inverse of a mux
A binary decoder with an enable input can be used as a Demux. E.g. 74x139 can be used as a 2-bit, 4-output Demux

## Slide 37: Logic functions using MUX

## Slide 38: Logic functions using MUX

## Slide 39: Logic functions using MUX
Example: Implement the following with a MUX and any additional logic gates
A | B | X
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1

## Slide 40: Logic functions using MUX
3 inputs XOR can be done with 2 2-to-1 MUX

## Slide 41: Logic functions using MUX
Example: Implement the following with a MUX and any additional logic gates
A | B | C | X
0 | 0 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 42: Shannon’s expression theorem
Any boolean function f(w1,w2, …, wn) can be written in a form:
f(w1,w2, …, wn)=*f(0,w2, ..., wn) + w1*f(1, w2, …wn)
This can be done with any of the n variables

## Slide 43: Shannon’s expression theorem
Example 1:
f(w1,w2, w3)= w1w2 + w1w3 + w2w3
Expanding this in terms of w1:
f(w1,w2, w3)= w1(w2 + w3) + (w2w3)
f when w1=1
f when w1=0
Wrong??

## Slide 44: Shannon’s expression theorem

## Slide 45: Shannon’s expression theorem
Example 2:
Choose x as the expansion variable

## Slide 46: Shannon’s expression theorem
Example 3:
            Choose z as the expansion variable

## Slide 47: Example
Using 4-1 mux and essential logic gates to implement this function:
  F (a, b, c, d) = SOP (1, 3, 5, 6, 8, 11, 15)
Requirement: c and d are control inputs of the 4-1 mux

## Slide 48: 5.7 Parity Generator/ Checker

## Slide 49: Exclusive OR and Exclusive NOR Gates
XOR:
XNOR:
Truth Table : XOR X Y XOR XNOR 0 0 0 1 0 1 1 0 1 0 1 0 1 1 0 1 XNOR
X
Y
F
X
Y
F

## Slide 50: XOR and XNOR Symbols
Equivalent Symbols of XOR gate
Equivalent Symbols of XNOR gate
For both XOR, XNOR: Any 2 signals (inputs or outputs) may be complemented without changing the resulting logic function

## Slide 51: XOR Application: Parity Circuit
Odd Parity Circuit: The output is 1 if odd number of inputs are 1
Even Parity Circuit: The output is 1 if even number of inputs are 1
Example: 4-bit Parity Circuit
I0
I1
I2
I3
ODD
EVEN
I0
I1
I2
I3
ODD
EVEN
Input: 1101 Odd Parity output: 1 Even Parity output: 0
Daisy-Chain Structure
Tree structure

## Slide 52: MSI Parity Circuit : 74x280

## Slide 53: Parity checker

## Slide 54: 5.8 Comparator

## Slide 55: Comparator
Comparator circuit compares two inputs
  Produces 1 if they are equal
  Produces 0 if they are not equal
Based on Exclusive-OR gate, returns 0 if the inputs are equal and 1 if they are unequal
A NOR gate decides whether to return 1 for equality or 0 for inequality

## Slide 56: 1 bit comparator
a | b | gt | eq | lt
0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 1
1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 1 | 0

## Slide 57: 4 bit comparator
eq

## Slide 58: 4 bit comparator
gt

## Slide 59: 4 bit comparator

## Slide 60: 4 bit comparator
The 7485 is a standard comparator package with the following attributes:
if (A>B) lt=0, eq=0, gt=1
if (A<B) lt=1, eq=0, gt=0
if (A=B) lt=l, eq=e, gt=g
Note: The three l, e and g inputs are used when cascading

## Slide 61: 16 bit comparator
Cascading 4 7485 to construct a 16 bit comparator

## Slide 62: 16 bit comparator
This comparator will first compare the 4 most significant bits of the two inputs
in this first stage
  ‘a’ is less than ‘b’ if a’s 4 MSB are smaller
  ‘a’ is greater than ‘b’ if the 4 MSB are larger
  If these 4 MSB of the two numbers turn out to be equal, the final result is from less significant bits comparison

## Slide 63: Example
Design a maximum, minimum finder of n 4 bit numbers using comparators and MUXs

## Slide 64: Any question?