## Slide 1: Latches and Flip-Flops
01/2013
Phan Quốc Huy

## Slide 2: Content
6.1 SR Latch
6.2 D Latch
6.3 Flip-flops
Reading assignment:
Chapter 7 (section 7.1, 7.2)

## Slide 3: Bistable Elements

## Slide 4: Bistable element
The simplest sequential circuit
Two states
  One state variable, say, Q, two possible states
  no way to control its state
HIGH
LOW
LOW
HIGH
LOW
HIGH
HIGH
LOW

## Slide 5: Analog analysis
Assume pure CMOS thresholds, 5V rail
Theoretical threshold center is 2.5 V
2.5 V
2.5 V
2.5 V
2.0 V
2.0 V
4.8 V
2.5 V
2.51 V
5.0 V
0.0 V
0.0 V
5.0 V

## Slide 6: Metastability
Metastability is inherent in any bistable circuit
Two stable points, one metastable point

## Slide 7: Another look at metastability

## Slide 8: Why all the harping on metastability?
All real systems are subject to it
  Problems are caused by “asynchronous inputs” that do not meet flip-flop setup and hold times
Severe in high-speed systems since clock periods are so short, “metastability resolution time” can be longer than one clock period
Many digital designers, products, and companies have been burned by this phenomenom

## Slide 9: Back to the bistable….
How to control it?
  Control inputs
S-R latch

## Slide 10: Latches and Flip flops

## Slide 11: The Set-Reset Latch
Q
S
R
Q’
Q
Q’
R
S
FF

## Slide 12: The Set-Reset Latch
P
Q
S
R
If S=0 and R=0, what are
the stable states for this
circuit?
(i) Assume P=0;
0
0
0
P=0 and Q=1 is stable
1

## Slide 13: The Set-Reset Latch
P
Q
S
R
If S=0 and R=0, what are
the stable states for this
circuit?
(i) Assume P=0;
0
0
1
(ii) Assume P=1;
P=0 and Q=1 is stable
0
P=1 and Q=0 is stable

## Slide 14: The Set-Reset Latch
P
Q
S
R
If the state is P=1 and Q=0,
and the input S changes to
1, what happens?
0
0
1
0
1
0
1
The new stable state is
P=0 and Q=1
What happens if S changes
to zero now?
0
The state does not change!

## Slide 15: The Set-Reset Latch
P
Q
S
R
If the state is P=0 and Q=1,
and the input R is changed to
1, what happens?
0
0
0
1
1
1
0
The new stable state is
P=1 and Q=0
What happens if S changes
to zero now?
0
The state does not change!

## Slide 16: The Set-Reset Latch
Therefore:
  if S changes to 1 for a short period of time,
  the flip-flop goes to the state P=0, Q=1;
  if R changes to 1 for a short period of time,
  the flip-flop goes to the state P=1, Q=0;
  We consider Q to be the output of the latch, therefore S is the “Set” input, and R is the “Reset” input.
What happens if R and S are 1 at the same time?

## Slide 17: The Set-Reset Latch
P
Q
S
R
Lets assume that P=0, Q=1
initially and then R and S
become 1.
0
0
0
1
1
1
0
The new stable state is
P=0 and Q=0
But this is no longer a latch because
P is no longer a complement of Q!
S=1 and R=1 is not allowed

## Slide 18: The Set-Reset Latch
Q
Q’
R
S
FF
S(t)
R(t)
Q(t)
1
1
1
X
X
Q(t+) = S(t) + Q(t)R’(t)

## Slide 19: S-R latch operation
Metastability is possible if S and R are negated simultaneously.

## Slide 20: S-R latch timing parameters
Propagation delay
Minimum pulse width

## Slide 21: S-R latch symbols

## Slide 22: S-R latch using NAND gates

## Slide 23: S-R latch with enable

## Slide 24: Using an enable S-R latch to build a Trigger Latch
T




Q
T
S’
R’’
S’
R’
FF
Q
Q’
T
What happens if the
T input is at 1
for a longer time?
The flip-flop oscillates
until T goes back to 0.

## Slide 25: D latch

## Slide 26: D-latch operation

## Slide 27: D-latch timing parameters
Propagation delay (from C or D)
Setup time (D before C edge)
Hold time (D after C edge)

## Slide 28: Edge-triggered D flip-flop behavior

## Slide 29: Edge-triggered D flip-flop behavior

## Slide 30: FF vs. Latch
Latches and flip-flops (FFs) are the basic building blocks of sequential circuits.
  latch: bistable memory device with level sensitive triggering (no clock), watches all of its inputs continuously and changes its outputs, independent of a clocking signal.
  flip-flop: bistable memory device with edge-triggering (with clock), samples its inputs, and changes its output only at times determined by a clocking signal.

## Slide 31: D flip-flop timing parameters
Propagation delay (from CLK)
Setup time (D before CLK)
Hold time (D after CLK)

## Slide 32: Other D flip-flop variations
Negative-edge triggered
Clock enable

## Slide 33: D FF with asynchronous inputs
Force the D FF to a particular state independent of the CLK and D inputs
  PR (Preset) and CLR (Clear)

## Slide 34: J-K flip-flop

## Slide 35: T (toggle) flip-flop
Change state on every stick of the lock
How to build a T FF using?
  D FF
  J-K FF

## Slide 36: Notes
When power is applied, it is not possible to predict the starting state of a flip-flop’s output
  If SET and RESET inputs are in their inactive state
To start a latch or FF in a particular state, it must be placed in that state by momentarily activating the SET or RESET input, at the start of operation
  Often achieved by application of a pulse to the appropriate input

## Slide 37
Any question?